## Slide 1: Data-driven Predictive maintenance
Data Mining
Rahma Dawud
Gessesse Dagmawi Sahleslassie

## Slide 2: Maintenance management
Reactive maintenance:
  Simple
  Very high down time and cost of intervention
  Safety concern
Preventive (Periodic) maintenance
  Failures are usually prevented
  Unnecessary corrective actions
  Inefficient use of resources
Predictive maintenance
  Enables timely pre-failure interventions
  Increases productivity
  Allows optimal planning of service interventions and spare part handling
Complexity and efficiency
source: https://leanbi.ch/blog/predictive-maintenance-wie-starten/
Fig. 1 Types od maintenance

## Slide 3: Goal
  Develop a machine learning model to predict the probability that a machine will fail due to a certain component within a specified time (48 hours)

## Slide 4: About The Data
Four data sources
  Telemetry data: Sensor data of voltage, rotation, pressure, vibration
  Error :Errors encountered by the machines while in operating condition (5 types)
  Maintenance: Historical maintenance records (4 components)
  Machine: Machine information (model, type, age)
  Failures: Each record represents replacement of a component due to failure
Microsoft Azure dataset
  100 Machines
  Hourly time series data for 1 year
  876,100 records
https://www.kaggle.com/datasets/arnabbiswas1/microsoft-azure-predictive-maintenance

## Slide 5: Steps to prediction
Exploratory data analysis (EDA)
Identify patterns, trends, and relationships among the variables in the data.
Feature engineering
Bringing the different data sources together to create features that best describe a machines' health condition
Lag features for long- and short-term dependencies
Rolling aggregate measures (mean, standard deviation)
Days since last replacement
Modeling
Multi class classification problem
4 component failures + No failure
A time window of 48 hrs
Select a suitable ML algorithm
Class imbalance problem
Evaluation
Find the appropriate metric
Recall (Sensitivity, True positive rate) is a good performance measure)

## Slide 6: Exploratory Data Analysis

## Slide 7: telemetry data
Telemetry data ranges from: 2015-01-01 06:00:00 to 2016-01-01 06:00:00
Total number of telemetry records: 876100
voltage, rotation, pressure, vibration
Fig. 2 Time series plot for machine id 1

## Slide 8: telemetry data: Timeseries decomposition
Observation
  Peaks in the trend
  Seasonality
Fig. 3 Timeseries decomposition of vibration
First 30 days

## Slide 9: telemetry data: Distribution
Observation
  No Missing values
  No duplicates
  There are a few spikes may be due to sensor malfunction
  All telemetry variables have a normal distribution
  There are a few outliers
Fig. 4 Histogram and box plot for voltage

## Slide 10: Error data
Fig. 5 Distribution of Error Types
Observation
  Error1 and error2 are the most common errors
  Error5 is the least common

## Slide 11: Failures DATA
Fig. 6 Distribution of component failures
Observation
  Component 2 is the most frequently
  Component 3 seems relatively stable

## Slide 12: EXPLORTORY DATA ANALYSIS FAILURES DATA
Fig. 7 Top 10 machines with the most failures
Observation
Machine ID 99 with the most failure

## Slide 13: Machines metaData
Fig. 8 Machines model and age
Machine ID 99 with the most failure
Observation
More than 60 percent of the machines are of model 3 and 4
The age ranges from 0 to 20 years.

## Slide 14: Feature engineering
create features that best describe a machines' health condition

## Slide 15: LAG FEATURES FROM TELEMETRY
Create features using rolling mean and standard deviation
Selected window sizes for each of the telemetry variables
  Short term dependencies: 4 hours
  Long term dependencies: 48 hours

## Slide 16: LAG FEATURES FROM ERRORS
Errors are categorical
Count the number of errors of each type in a lagging window (48 hours)
datetime | Error
01.04.15 08:00 | error1
05.04.15 12:00 | error4
06.04.15 12:00 | error1
Errors table
datetime | error1_48h_sum | error2_48h_sum | error3_48h_sum | error4_48h_sum | error5_48h_sum
01.04.15 06:00 | 0 | 0 | 0 | 0 | 0
02.04.15 07:00 | 0 | 0 | 0 | 0 | 0
03.04.15 08:00 | 1 | 0 | 0 | 0 | 0
04.04.15 09:00 | 1 | 0 | 0 | 0 | 0
05.04.15 10:00 | 1 | 0 | 0 | 0 | 0
06.04.15 11:00 | 1 | 0 | 0 | 0 | 0
07.04.15 12:00 | 2 | 0 | 0 | 1 | 0
08.04.15 13:00 | 2 | 0 | 0 | 1 | 0
09.04.15 14:00 | 2 | 0 | 0 | 1 | 0
10.04.15 15:00 | 2 | 0 | 0 | 1 | 0

## Slide 17: LAG FEATURES Maintenance
Number of days since Last component replacement
Maintainance table

## Slide 18: Target variable Construction
Failure data
Create a multi-class label with a 48h window
Possible classes
Normal, comp1, comp2, comp3, comp4
Fig. 11 Distribution of failures

## Slide 19: Modeling anD EVALUATION
A multi-class classifier

## Slide 20: Modelling and Evaluation
A multi-class classification problem
Dealing with class imbalance
Selecting the right algorithm
Selecting the right metrics
Hyperparameter optimization